## Slide 1: Progress on a Multiphysics Approach for Predicting Reactivity Feedback due to Fast Reactor Core Bowing
Nick Wozniak, Gang Yang, Yiqi Yu, Ahmed Abdelhameed, Emily Shemon
Argonne National Laboratory
nwozniak@anl.gov
May 29, 2025
NEAMS Annual Review: Fast Reactors

## Slide 2: Fast Reactor Core Bowing Phenomenon
Motivation: Fast reactors are highly sensitive to neutron leakage. Thermal bowing and irradiation creep and swelling cause assemblies to deform and bow in different configurations
  Core restraint system guides the amount of bowing and the shape of each assembly
  Reactivity feedback from assembly movement should be negative during accidents
  Assembly handling loads at refueling must be kept reasonable despite bowing
Understanding of core bowing comes from EBR-I, EBR-II, and FFTF
Limited free-bow core restraint system concept showing radial expansion in the core region1
Cold zero power
Hot full power
1. J. J. Grudzinski and C. Grandy, “Fuel Assembly Bowing and Core Restraint Design in Fast Reactors,” in Proceedings of the ASME 2014 International Mechanical & Engineering Congress & Exposition, Montreal, Canada: ASME, Nov. 2014, p. V06BT07A026. doi: 10.1115/IMECE2014-38331.
ACLP
TLP
Restraint
Active Core
Notes: Mention the curved shape of assemblies
Core region deforms outward, and gaps expand (lower reactivity feedback)
Restraint ring helps drive maximum outward bowing
KEEP IT SHORT

## Slide 3: Advanced Mod/Sim Objectives
Objective: Leverage MOOSE multiphysics framework-based tools to directly model core bowing and reactivity feedback. There is no present capability to do this, although previous efforts under NEAMS demonstrated feasibility of the concept2.
Existing Approaches
NUBOW-3D + Perturbation theory
  Beam model bending, low fidelity
  Offline coupling, file transfer
SAS4A/SASSYS-1
  Simple radial expansion model, no bowing
  Detailed radial expansion with bowing, uses average assembly
SAM with Point Kinetics
  Simple radial expansion model, no assembly bowing
  Coupling with Structural Mechanics
2. E. Merzari et al., “Multi-Physics Demonstration Problem with the SHARP Reactor Simulation Toolkit,” Argonne National Lab. (ANL), Argonne, IL (United States), ANL/NE-15/44, Dec. 2015. doi: 10.2172/1236454.
Proposed Approach
Notes: Delineate the different approaches
How is fuel temperature calculated – developing built-in capability in SC module
MOOSE Approach to directly model deformation reactivity
SAS
Simple Model: “The simple model calculates the average radial expansion at the core midplane assuming straight line expansion between the above core load pads and the grid plate. Because straight line expansion is modeled, this model only considers thermal expansion.”
Detailed Model: “The detailed model calculates the axial profile of the core radius from the behavior of an average assembly. All assemblies are assumed to move radially in proportion to their distance from the core centerline. This model accounts for thermal expansion and assembly bowing.”
SAM: Takes into consideration different contributions of the inlet grid plate and above core load pad expansions.

## Slide 4: Multi-Year Roadmap
Chart: 
| TM Assessment | TF and TM Coupling | RP Assessment | TF Assessment | RP, TF, and TM Coupling | Demonstration Problems
Start Date | 2022 | 2024 | 2024 | 2025 | 2025 | 2026
Duration | 4 | 1 | 2 | 1 | 1 | 3
IAEA VPs for core bowing
7 & 19 asmbly
US-Japan bilateral benchmark
SAM vs.SC
7 & 19 asmbly
Increase core size, SS, startup, transient
Today
TM: Thermo-mechanics
TF: Thermal fluids
RP: Reactor Physics
Notes: This is showing FY dates
Ending dates for some of the tasks aren’t firmly set, they are variable
  V&V of MOOSE’s thermo-mechanical solvers specifically for this application
  V&V of Griffin for this application, and comparison to conventional perturbation-based approach (US-Japan CNWG partnership)
  Multiphysics coupling of thermo-mechanics, thermal fluids, and reactor physics in a staged process to allow code developers time to incorporate feedback
  Provide “predictive” reference solution to determine regimes of validity of faster running, more approximate methods

## Slide 5: Solid Mechanics Assessment
Current assessment focuses on more realistic limited free-bow design4
  Thermal gradient applied to 5th ring of ducts causing outward bowing
  S-shaped curve observed in agreement with study participant results
Reactor sector displacement
Duct 44 centerline displacement
IAEA VP4 Thermo-mechanical model with symmetric sector bowing3 (© IAEA)
4. N. Wozniak, et al (2024). Demonstration and Verification of Thermo-Mechanical Bowing in a Limited Free-Bow SFR Concept Using MOOSE. Transactions of the American Nuclear Society, 131(1), 1010-1013.
Previous assessments used IAEA verification problems3 to verify thermo-mechanical behavior of duct bowing, load pad contacts, irradiation creep and swelling behavior
Explicitly modeled load pads and contact with penalty contact, node-on-face algorithm in MOOSE Contact Module
3. “Verification and Validation of LMFBR Static Core Mechanics Codes Part I,” International Atomic Energy Agency, Vienna, IWGFR/75, 1990.
Notes: Mention complexity of modeling the duct, non-uniform expansion, bending, nozzle, contacts at load pads

## Slide 6: Thermal Fluids + Thermo-Mechanics Coupling Demo: 7 assembly
MOOSE Heat Conduction
MOOSE-SC
MOOSE Solid Mechanics
Heat Flux
Temperature
Duct-wall Temperature
Coupled approach (without reactor physics)
Force asymmetric power profile in center assembly
Computed duct-wall temperature and thermal displacement
ACLP
TLP
Outward Bowing
Inward Bowing
Radial deflection of center assembly as a function of axial location5
Seven ABR-1000 fuel assemblies, no restraint ring
Radial power gradient forced in center assembly to drive duct wall temperature gradient and bowing
5. G. Yang, et al (2024) Multiphysics Demonstration of Temperature-Driven Assembly Bowing in SFRs using MOOSE-Based Codes. Transactions of the American Nuclear Society, 131(1), 1006-1009.
1
2
3
4
7
5
6
Notes: 7-assembly model was developed using fuel assemblies from the ABR-1000 design, including load pads, in a hexagonal lattice of 2 rings4
The assembly total power is set to the average power of an ABR-1000 fuel assembly (5.56 MW).
Cosine power shape is assumed in the axial direction.
Center assembly: radially asymmetric power distribution (asymmetry drives temperature gradient across duct which drives asymmetrical expansion/bowing)
Peripheral assemblies: uniform radial power distribution
Swirl of wire-wrap, causes rotational deformation of duct at different axial levels

## Slide 7: Thermal Fluids + Thermo-Mechanics Coupling Demo: 19 assembly
Computed duct-wall temperature and thermal displacement
ACLP
TLP
Outward Bowing
Inward Bowing
Radial deflection of assembly 6 as a function of axial location6
Solid Mechanics Mesh
Load Pad Locations
6. N. Wozniak, et al, “MOOSE-Based Fast Reactor Core Bowing Capabilities: Coupled Structural Mechanics – Thermal Fluids Demonstration and Related Verification Efforts,” ANL/NEAMS--24/2, 2447921, 191719, Sep. 2024
19 ABR-1000 fuel assemblies, no restraint ring
Radial power gradient forced in assembly 6 to drive duct wall temperature gradient and bowing
1
2
3
4
7
5
15
9
11
6
10
8
12
13
14
16
17
19
18
Force asymmetric power profile in assembly 6
Notes: Best practices modeling contact

## Slide 8: Thermal Fluids and Thermo-mechanics Coupling Findings
Coupled thermal fluids & thermal mechanics using MOOSE modules for calculating duct thermal bowing with reasonable prediction of bowing behavior and inter-assembly contact
MOOSE-SC can predict the detailed duct wall temperature distribution with asymmetric power profile, including impact of wire wrap on flow
Heat conduction model is used for inter-assembly gap heat transfer, but does not include inter-assembly flow modeling
Also performed SAM calculations for comparison
  Duct wall temperature prediction with SAM multichannel model agrees well with CFD and MOOSE-SC calculations. SAM may be a promising option for coupling with neutronics and solid mechanics modules for long term transient simulations.
  SAM Point Kinetics Model will be used as a low fidelity reference to compare with the integrated multiphysics approach.
Notes: NEAMS TH Area is working on inter assembly flow modeling

## Slide 9: Current Year: Integration of Reactor Physics into Coupled Thermal Fluids + Thermal Mechanics Workflow
Duct and inter-assembly coolant gaps explicitly modeled to capture neutron leakage induced by core bowing
  Will utilize “duct-het” and “ring-het” representations available in Griffin (with automated fast reactor cross section workflows)
Pin powers will be reconstructed in Griffin and transferred to MOOSE-SC to solve for temperature distribution
Griffin’s mesh will be deformed to calculate new reactivity state
  Additional logic in Griffin will be required to “back-fill” sodium coolant with the correct density into homogenized regions
Since FY24, we participate in a joint reactor physics benchmark with JAEA under the US-Japan CNWG bilateral. Aim is to understand and compare reactor physics approaches to modeling fast reactor core deformation.
Notes: Don’t want to throw Griffin under the bus
Just starting integration
We have a path we think will work, but haven’t done it yet, how next to proceed

## Slide 10: Summary
Core bowing, guided by the core restraint system, is an important passive safety feature in LMFRs
We are developing an integrated multiphysics approach using the MOOSE framework to directly model reactivity feedback in LMFRs due to core bowing.
  The proposed approach will offer a high-fidelity reference solution capability – can benchmark faster running approaches as well as perform detailed analysis for restraint system performance
Completed: several thermo-mechanical benchmarks for core bowing behavior, thermal fluids/thermo-mechanical coupling small core demonstration problems (without restraint rings)
In progress: reactor physics & thermal fluids verification, reactor physics integration, modeling of restraint ring
Future: application of code suite to full core problems, start up, and transients. Working with ART FRP to identify and obtain suitable validation data.
Notes: Why do we need high fidelity approach to core bowing and reactivity feedback, how to convince
Specific accident scenarios are important to more accurately calculate the core response

## Slide 11: Acknowledgement
This research made use of the resources of the High Performance Computing Center at Idaho National Laboratory, which is supported by the Office of Nuclear Energy of the U.S. Department of Energy and the Nuclear Science User Facilities under Contract No. DE-AC07-05ID14517.

## Slide 13: 7-Assembly Coupled Model
7-assembly model was developed using fuel assemblies from the ABR-1000 design, including load pads, in a hexagonal lattice of 2 rings4
  The assembly total power is set to the average power of an ABR-1000 fuel assembly (5.56 MW).
  Cosine power shape is assumed in the axial direction.
  Center assembly: radially asymmetric power distribution (asymmetry drives temperature gradient across duct which drives asymmetrical expansion/bowing)
  Peripheral assemblies: uniform radial power distribution
4. Yang, G., Wozniak, N., Shemon, E., & Spencer, B. (2024). Multiphysics Demonstration of Temperature-Driven Assembly Bowing in SFRs using MOOSE-Based Codes. Transactions of the American Nuclear Society, 131(1), 1006-1009.
7-assembly model configuration

## Slide 14: 19-Assembly Coupled Model
19-assembly model was developed by extending the 7-assembly model with an outer ring of assemblies
  Assembly 1 is assigned the highest power (6.95 MW)
  Assemblies 2 – 7 are set to the average power of an ABR-1000 fuel assembly (5.56 MW).
  Outer ring is assigned a lower power (4.17 MW)
  Cosine power shape is assumed in the axial direction.
  Radially asymmetric power distribution assigned to assembly 6 (asymmetry drives temperature gradient across duct which drives asymmetrical expansion/bowing)
  Peripheral assemblies: uniform radial power distribution
19-assembly model configuration and temperature distribution at the top surface
N. Wozniak, G. Yang, E. Shemon, and A. Abdelhameed, “MOOSE-Based Fast Reactor Core Bowing Capabilities: Coupled Structural Mechanics – Thermal Fluids Demonstration and Related Verification Efforts,” ANL/NEAMS--24/2, 2447921, 191719, Sep. 2024