## Slide 1: Release of NEML2 A High-Performance Constitutive Modeling Library
Gary Hu, ANL, thu@anl.gov
Mark Messner, ANL, messner@anl.gov

## Slide 2: Motivation
Challenge #1
  High-fidelity material models help ensure long-term structural integrity of reactor designs
    Plasticity, viscoplasticity, creep, etc.
    Multiscale reduced-order models
    Data-driven models
  Fidelity Cost
Chart: 
| Assemble equations | Solve | Material model
Cost | 4563 | 6410 | 25830
Challenge #2
  Most computing power in newly built HPCs are provided by GPUs.
  This trend mostly aligns with the rise of AI/ML.
  Can we use GPUs for tasks other than AI/ML, e.g., nuclear reactor simulations?
  Yes!
Supercomputer | Year | Performance | GPU Contribution (%)
Tianhe-1A | 2010 | 4.701 petaflops | ~60–70%
Titan | 2012 | 17.59 petaflops | ~85–90%
Summit | 2018 | 148.6 petaflops | ~95%
Sierra | 2018 | 125.7 petaflops | ~95%
ABCI | 2018 | 19.88 petaflops | ~90%
Perlmutter | 2021 | 70.9 petaflops (Phase 1) | ~90–95% (GPU nodes)
Aurora | 2024 | ~2 exaflops (projected) | ~90%+
El Capitan | 2024 | ~2+ exaflops (projected) | ~95%

## Slide 3: NEML2
Publicly released: https://applied-material-modeling.github.io/neml2/
Feature highlights:
  A rich collection of extensible common material models for structural assessment of reactors
  Drop-in replacement for native material models in MOOSE
  Models are fast and scalable, and can run on both CPU and GPU
  Automated material model calibration/tuning against data
  A Python wrapper that is fully interoperable with PyTorch models

## Slide 4: Timing Results: NEML2
Crystal plasticity
50,000 grains
250 steps
111 pole figures
Chart: Wall clock time (s)
| Wall time (s)
NEML (CPU) | 42500
NEML2 (CPU) | 15000
NEML2 (GPU) | 120

## Slide 5: Timing Results: NEML2 + MOOSE
100 steps
64,000 constitutive updates per step
Chart: Wall clock time (s)
| NEML2 GPU | NEML2 CPU | NEML
Residual + Jacobian | 4486.07 | 4563.96 | 4563.96
Data transfer across devices | 916.855 | 1435.13 | 0
Material model | 400.6 | 13794.027 | 28530
Solve | 4008.679 | 4008.505 | 6410.707
Everything else | 1674.415 | 1423.378 | 2600

## Slide 6: Automated Material Model Calibration
Exercise: Calibrate a universal material model for various metallic alloys of interest.
  Completed: 316H, Grade 91, A800H, A617, Alloy 709
  In progress: 304H, Grade 22, ...
Technical report ANL-ART-284

## Slide 7: Conclusion and Future Work
Publicly released: https://applied-material-modeling.github.io/neml2/
Feature highlights:
  A rich collection of extensible common material models for structural assessment of reactors
  Drop-in replacement for native material models in MOOSE
  Models are fast and scalable, and can run on both CPU and GPU
  Automated material model calibration/tuning against data
  A Python wrapper that is fully interoperable with PyTorch models
Future work
  Implement work dispatchers for hybrid computing environments
  Explore the possibility of supporting Abaqus UMAT/VUMAT
Gary Hu thu@anl.gov
Mark Messner messner@anl.gov