## Slide 1: Heat Pipe Modeling Capabilities in Sockeye
Joshua Hansel Idaho National Laboratory

## Slide 2: Sockeye Overview
Engineering-scale heat pipe application based on MOOSE framework
Use cases:
  Heat pipe design studies
  Prediction of heat pipe performance limits
  Prediction of heat pipe transient response
  Prediction of heat pipe thermal resistance
Simulations may be standalone or multiphysics:
  Heat pipe microreactors

## Slide 3: Supported Heat Pipes
Supported wick designs:
  Conventional heat pipes with mesh screen wicks, with or without gap
  Not yet supported: wickless heat pipes, i.e., thermosyphons
Supported working fluids:
  Sodium
  Potassium
  Water
Screen wick with gap
Screen wick without gap
Vapor Wick Gap Wall

## Slide 4: Available Models
Two-phase flow model
1D, single-phase, compressible flow for vapor phase:
  Euler equations of gas dynamics
Rarefied gas flow treatment during startup
2D heat conduction used for liquid
Supports non-condensable gases
Thermally expanding condenser pool
Fairly robust
Vapor: 1D flow Liquid/wick: 1D flow
Wall: 2D heat conduction
Liquid-conduction, Vapor-flow (LCVF) model
Conduction model
Vapor: 1D flow Liquid/wick: 2D heat conduction
Wall: 2D heat conduction
Vapor: 2D heat conduction Liquid/wick: 2D heat conduction
Wall: 2D heat conduction
1D, two-phase, compressible flow:
  Baer-Nunziato equations
Not robust in single-phase regimes:
  Condenser pool
  Dryout
2D heat conduction in all regions
Uses analytic heat pipe limits
Controls vapor core thermal conductivity to enforce limits
Extremely robust

## Slide 5: Limits Support
Limit | Two-Phase Model | LCVF Model | Conduction Model | Notes
Capillary | Mechanistic | Mechanistic vapor, analytic liquid | Analytic | 
Sonic | Mechanistic | Mechanistic | Analytic | 
Viscous | Mechanistic | Mechanistic | Analytic | 
Entrainment | Not considered | Not considered | Analytic | Believed not to be a concern for high-temperature HPs.
Boiling | Not considered | Not considered | Analytic | Requires very high radial heat flux; not highest priority

## Slide 6: Verification
Sonic Limit
Capillary Limit Without Wick Gap
Capillary Limit With Wick Gap

## Slide 7: Validation Summary
Experiment | Fluid | Wick(s) | Cooling | Angle | Measurements | Status
RPI | H2O | Thermosyphon, Screen | Water HX | 90 | Fiber optics, TCs, Pressure, film thickness | O
SAFE-30 | Na | Screen | Radiation | 0 | TCs | C
SPHERE (2021) | Na | Screen | Radiation | 0 | Thermowell TCs, cooling rate | C
SPHERE (2023) | Na | Screen | Water HX | 0 | TCs, cooling rate | C
SPHERE (2024) | Na | Screen | Radiation to water HX | 0 | TCs, cooling rate | C
Texas A&M | H2O | Screen | Water HX | 0 | Fiber optics, TCs | O
U. Michigan | Na | Screen | Water+air HX | 0 | TCs, cooling rate | C
U. W-Madison | Na | Screen | Gas HX | 0 | Fiber optics, TCs, x-ray | P
Status: C = Complete, O = Ongoing, P = Planned

## Slide 8: Validation Case: SAFE-30
Two-phase model
LCVF model
Conduction model

## Slide 9: Validation Case: University of Michigan

## Slide 10: Some Other Validation
Faghri
Ivanovskii

## Slide 11: Multiphysics Demonstration
Demonstrated coupling of heat pipe models to microreactor block monolith
General-purpose heat pipe microreactor: 20 MWth with 876 heat pipes
Loss of heat sink transient
Steady core temperature

## Slide 12: Conclusions and Possible Future Work
Conclusions:
  Sockeye is a flexible, engineering-scale tool for the design and analysis of heat pipes, used in
    Single heat pipe studies
    Multiphysics simulations of heat-pipe-cooled microreactors
  The LCVF model is recommended for most applications due to its robustness and accuracy
Possible future work:
  Addressing phase disappearance in two-phase heat pipe model
  Supporting additional heat pipe types, e.g., thermosyphons
  Support for entrainment and boiling limits in flow models
  Continued validation, including additional experiments by the Microreactor Program