## Slide 1: Validation and sensitivity analysis of T/H capabilities for modeling of transient dry out and re-wet
Vineet Kumar, Bob Salko, and Will Gurecky
NEAMS ANNUAL REVIEW LWR
May 7, 2025

## Slide 2: Introduction
The T/H technical area seeks to support improved economics of the current LWR fleet by improving modeling accuracy, fidelity, and uncertainty
US nuclear industry is pursuing time-at-temperature strategy, allowing for limited fuel dryout during LWR transients
  Power uprates, operational flexibility, cost savings
  T/H modeling improvements are needed
Overview of NEAMS strategy for time-at-temperature
Cladding behavior during dryout/re-wet event

## Slide 3: T/H Assessment Strategy
How can NEAMS support stakeholders in t@T deployment?
Formal identification and ranking of phenomena importance
Quantify accuracy and uncertainty of available models
Develop new models for high uncertainty, high impact phenomena
Develop high-fidelity, multiphysics reference solutions with uncertainty
Identify relevant experimental data
Perform validation
Identify high impact models through sensitivity analysis
Quantify model uncertainty
Improve models as needed

## Slide 4: CTF
CTF is a three-field, two-fluid subchannel code derived from COBRA-TF
Validation matrix to support modeling of several applications:
  Depletion in PWRs and BWRs
  PWR RIA
  PWR LBLOCA reflood
Time-at-temperature requires new assessment campaign
  Validation for dryout and re-wet
  Identify high-impact phenomena/models
  Quantify model uncertainty

## Slide 5: Addition of new validation tests
Summary of current tests being considered for validation
CTF legacy post-CHF model
COBRA/TRAC post-CHF model
Implementation of new post-CHF package improves prediction of BFBT critical power
Data is critical to model UQ and new data sources are being pursued

## Slide 6: Addition of new validation tests
Development of ML CHF model improves prediction1
Harwell tests
  Dryout and post-CHF heat transfer in tube geometry with uniform heating
  Measurement of axial temperature profile
Dryout prediction improved with COBRA/TRAC heat transfer package
Reasonable dryout prediction for nominal BWR conditions
Axial temperature profile prediction
1. Physics-informed machine learning model developed by A. Furlong at NCSU in university collaboration leads to improved dryout prediction

## Slide 7: Validation testing: BFBT Turbine Trip
BFBT turbine trip simulates void collapse and power excursion
Reasonable prediction of void behavior
Failure to predict dryout
Consistent with bundle test behavior
1. Physics-informed machine learning model developed by A. Furlong at NCSU in university collaboration leads to improved dryout prediction
682 mm
CTF does not predict transition boiling

## Slide 8: Sensitivity analysis
Dryout and rewet requires complex interaction of several phenomena
Uncertainty of clad temperature behavior is needed
Most impactful phenomena and underlying models must be determined
Uncertainty quantification can be determined utilizing inverse UQ
Feed forward UQ will be performed for AOOs of interest using these findings
CTF models for dryout behavior

## Slide 9: Sensitivity analysis
CTF sensitivity parameters used
First high-level, then low-level
Sobol method and Gradient Boosted Regression used to determine importance
Interfacial drag
Entrainment
CHF
Heat transfer (liquid)
Heat transfer (vapor)
Heat transfer (boiling)
Small bubble
Slug
Dispersed
Annular film
Annular drop
Annular film
Hot film
Bubbly
Quench front
CHF
Nucleate boiling
Inverted annular film boiling
Droplet impingement
Droplet radiative
Vapor convection
x
x
High level
Interfacial heat transfer
Low level

## Slide 10: Steady-state CHF: Harwell
High level analysis can eliminate parameters from consideration
Parameters of importance change based on flow conditions.
High level analysis can eliminate parameters from consideration
FOM: Dryout location
FOM: PCT
CHF model
Boiling heat transfer
Vapor heat transfer
CHF model
Boiling heat transfer
Vapor heat transfer

## Slide 11: BFBT Turbine Trip
Boiling heat transfer and CHF, set dryout criteria
Vapor convection heat transfer dominates PCT prediction
FOM: ∆Tw,rmse
Cases with lower boiling heat transfer, higher CHF, and higher vapor heat transfer leads to better agreement
Similar phenomena rankings determined for BFBT and Harwell
This highlights model in need of improvement, and the magnitude of changes needed

## Slide 12: IFA6131,2
Instrumented fuel rodlets in Halden test rig with very low flow
Vary flow to cause transient dryout and re-wet in 26 different tests
CTF now over-predicts PCT and duration
M. Limback and R. Ianiri, “Dryout Fuel Behavior Tests in IFA-613.1”, OECD Halden Reactor Project, HWR-493, 1997.
Y. Broy, W. Wolfgang and L. A. Moen. “The OECD Halden Reactor Project-international research on safety and reliability of nuclear power generation.”, 2001.
Case 6
Case 11
Case | LHGR [kW/m] | Subcooling [K] | DO time [s]
6 | 13.6 | 51 | 3
11 | 7.0 | 55 | 47
Opposite trend of BFBT TT highlights the importance of test conditions

## Slide 13: Surrogate building
Use Bayesian inference to formally quantify model uncertainties using experimental data
Requires huge number of simulations O(100k)
Generating code surrogates may be needed to ensure reasonable turnaround time
Testing building surrogates for BFBT, Harwell, IFA613
BFBT turbine trip
Harwell
BFBT prediction of dryout occurrence

## Slide 14: Conclusions
NEAMS is employing a strategy to support t@T deployment
  Using advanced sensitivity and UQ techniques to quantify phenomena importance and model uncertainty
  Performing validation to assess model accuracy
  Improving on high uncertainty, high impact models
  Supporting high-fidelity, multiphysics modeling of relevant transients for t@T
Preliminary sensitivity analysis and validation has been performed to assess model accuracy and determine important models
Phenomena of high importance are beginning to emerge, but further consideration of the range of testing conditions is needed

## Slide 15: Future activities
Expand sensitivity analysis
  Cover all conditions of interest in Harwell
  Perform sensitivity analysis for BFBT pump trip test
  Perform refined analysis for all test cases
Expand validation
  BFBT pump trip, IFA613, UW HPHT tests
  JAERI 4x4 bundle tests and upcoming UW transient dryout tests are promising
  More data is always needed
Develop matrix of test conditions and model importance
Demonstrate the model UQ framework