## Slide 1: Enhancement on Species Transport Modeling in SAM and Coupling to Saline and Mole
Bob Salko, Travis Mui, Rui Hu
NEAMS ANNUAL REVIEW MSR
May 28, 2025

## Slide 2: Introduction
  A modern system analysis code for advanced non-LWR safety analysis
  Covers almost all non-LWR concepts
Ongoing efforts to develop SAM for MSR applications
  Salt thermophysical properties
  Salt freezing
  Species tracking for delayed neutron precursors and fission products in both salt and sparge gas
  Species decay and decay heat
  Species phase transfer
  Modeling of non-condensable gas transport
Validation using MSRE, MSR Campaign data, and open two-phase data
Prediction of salt xe-135 distribution in MSRE1
T. Mui, et al. “SAM Code Improvements for Molten Salt Reactor Transient and Species Transport Modeling”, ANL/NSE-24/73, 2024.
Yoder, G., et al. “Development of a forced-convection liquid-fluoride-salt test loop”, Proceedings of HTR, 2010
Prediction of pressure distribution in LSTL2

## Slide 3: Species Tracking in SAM
Generic species (passive scalar) transport originally implemented in SAM to model flowing delayed neutron precursors in MSRs
Framework expanded to simulate transport pathways of tritium in FHRs and MSRs
Ongoing work to consider additional applications:
  Oxidation-corrosion in lead-cooled reactors
  Redox corrosion in salt-cooled reactors
  Noble gas/metal transport in MSR
Species transport pathways modeled in SAM

## Slide 4: Enhancements to Species Tracking
Species can now exist in the gas phase
  Transported by gas velocity
Phase transfer using Henry’s Law for high-volatile gas
  Henry and mass transfer coefficient calculated by Mole
  Interfacial area and gas velocity by SAM
Capture decay between species
Added phase transfer term
Track decay from one species to another
Gas/bubble behavior predicted by SAM
Species can exist in gas phase
Mass transfer data from Mole
vg
cg
cl
Phase transfer
ai
Iodine transport in liquid
Xenon transport in liquid
Xenon transport in gas
: Species velocity (m/s)
: Species decay coefficient (1/s)
: Liquid/gas phase index
: Mass transfer coefficient (m/s)
: Henry’s coefficient (mol/m3/atm)
: Universal gas constant (J/mol/K)
: Temperature (K)
: Iodine concentration (#/m3)
: Xenon concentration (#/m3)
: Interfacial area (m2/m3)

## Slide 5: Coupling to Saline and Mole
Mole provides modeling of high-volatile species phase transfer1
  Utilizes two-film theory
  Provides Henry coefficients for FLiNaK and FLiBe salts and several noble gases
  Mass transfer coefficient determined using Wilke-Chang or Stokes-Einstein1
Saline is a C++/Fortran/Python interface to MSTDB-TP
  Integrated into MOOSE and SAM
  Provides thermophysical properties of many common salts and salt compositions
Gas liquid interface modeled using two-film theory
Interface concentrations determined using Henry’s Law
1. K. Lee, W. Williams, J. McFarlane, D. Kropaczek, and D. de Wet, “Semi-empirical model for Henry’s Law Constant of Noble Gases in Molten Salts”, Nature Portfolio, 14:12847, 2024, https://doi.org/10.1038/s41598-024-60006-9.

## Slide 6: Verification and Validation Activities
McFarlane, J., et al. “Design of Instrumentation for Noble Gas Transport in LSTL Needed for Model Development” Report. ORNL TM-2023-3138 (2023).
Yoder, G., et al. “Development of a forced-convection liquid-fluoride-salt test loop”, Proceedings of HTR, 2010
Salko, R, et al. “Implementation of a Drift Flux Model into SAM with Development of a Verification and Validation Test Suite for Modeling of Noncondensable Gas Mixtures”, Nuclear Technology, 2024
Modeling of experiments of bubbles rising in molten salt1
Modeling of pressure drop in LSTL2
Modeling of void fraction in Kress experiment3
Development of verification test suite for gas transport model3

## Slide 7: Modeling of Off-Gas System
Model pool-type MSR
  Bubble generation due to xenon creation and phase transfer
  Species and bubble transport affects fission gas concentration in pool region
  Bubble buoyancy leads to escape at pool surface
Depletion determines fission product inventory
Coupled system being utilized for prediction of off-gas of fission products plus uncertainty1
DOE iFOA project in collaboration with Terrestrial Energy, USA

## Slide 8: Uncertainty Quantification of Offgas
Forward UQ analysis of off-gas modeling
  Variation of 15 input parameters
  Nuclear data, thermophysical fluid properties, mass transfer data, bubble behavior
  Xenon, cesium, and iodine off-gas rate are figures of merit (FOM)
  5,000 evaluations of coupled analysis lead to convergence of FOMs
Bubble velocity uncertainty obtained from MSR Campaign data1
D. Orea, K. Robb, J. McFarlane, “Comparative Study Between Experimental Measurements and Model Predictions of Bubble Rise Velocity in Molten LiCl-KCl”, in press., 2025
Spread in off-gas release rates due to input uncertainties
Relationship between input parameters and off-gas rates
Bubble terminal velocity, bubble diameter, and thermochemical data found to be potentially high importance

## Slide 9: Summary
Species and gas transport modeling capabilities expanded in SAM for modeling of MSRs
  Ability to track gaseous species using drift flux
  Ability model phase transfer, decay between species, and bubble release
Demonstration of capabilities shown by performing fission gas release uncertainty analysis
Model will be expanded including coupling with Thermochimica, bubble modeling improvements based on MSR Campaign data, graphite xenon absorption, and improved coupling for depletion