## Slide 2: Review of Running-In Simulation and Verification Efforts for Pebble-Bed Reactors
Presented by: Josh Hanophy
May 8, 2025
NEAMS Annual Review: HTGR & FHR

## Slide 3: Overview
Review important points about the running-in phase of operation
Overview of code-to-code verification methodologies
  Compare PBR modeling approach in Griffin versus kugelpy
Summary of important code-to-code verification results thus far

## Slide 4: Running-in – Overview
Pebble Bed Reactors (PBRs) start with graphite pebbles filled to a certain height then mix of fuel pebbles and graphite pebbles above this
  Graphite pebbles removed from core and replaced with fuel pebbles over time
  Power increased from zero to nominal operating level over period of approximately 1 year
Models can inform important questions
  How fast can reactor be brought to full power?
  What are core configurations with minimum safety margins?
0 days
3.3 days
6.7 days
10 days

## Slide 5: Running-in – Some Important Questions
Significant power spike seen when equilibrium fuel is first added
  Results from realistic model including multiphysics
Interested in seeing if similar predictions exist for both Griffin and kugelpy despite their significantly different modeling approaches
Sampe running-in results from a Griffin gas-cooled PBR model

## Slide 6: Pebble Bed Modeling with Streamlines in Griffin
Griffin is a deterministic transport code
  “Streamline” based approach to modelling pebble bed reactors
Griffin is a MOOSE based application
Major benefits of using Griffin
  Fast deterministic solves means transients and “quasi-static” transients like running-in simulation are very fast
  Multiphysics can be included in a simple and efficient way
Potential draw back of using Griffin
  Deterministic methods requires some method to attain multi-group cross sections
  Some question about what errors the homogenized streamline based modeling approach introduces
Streamline schematic and results for generic gas cooled PBR with lower cone modeled

## Slide 7: Kugelpy Running-In Overview
kugelpy is a Monte Carlo based code
Different from the approach in Griffin
  kugelpy models each pebble vs the homogenized approach in Griffin
  kugelpy implements a Lagrangian approach versus Eulerian in Griffin
  No numerical diffusion as pebbles move down in kugelpy
Serpent used for the studies so far
  Development team at ORNL currently integrating kugelpy with SHIFT
Example of critical height core configuration for the Kugelpy test model

## Slide 8: Code-to-Code Verification Study
Developed equivalent simplified models in both Griffin and Kugelpy
  Both codes perform depletion calculations with fixed temperatures (no multiphysics)
    Implementing multiphysics in Kugelpy still a research topic
    Enough complicated phenomenology to investigate initially without considering multiphysics
Particularly interested in comparing predictions for the spike in maximum power density when equilibrium fuel introduced
Simplified PBR for initial code-to-code validation studies
Griffin
kugelpy

## Slide 9: Initial Code-to-Code Testing
Three pebble types utilized for running-in studies
  Inert graphite pebble
  5% enriched starting fuel pebble
  15.5% enriched HALEU fuel
First study with simplified reactor model filled with 40%/60% mixture of graphite pebbles/fresh starting fuel
  Important to start with simple study since pre-generated multigroup library used in Griffin model was developed for equilibrium core
  Fresh core k-eff from kugelpy 1.07590±0.00036
  Griffin prediction is 1.07283, which is lower by approximately 300 pcm
Results from initial calculation with the core full or 40%/60% mixture of graphite pebbles/fresh starting fuel, power at 25 MW, and pebbles flow at 2 pebbles/minute

## Slide 10: Running-in Started from Sharp Interface
Verification studies started from a sharp interface between graphite pebble region and fueled region with fueled region having 40%/60% mixture of graphite pebbles/fresh starting fuel
Two sets of results reviewed next, both starting from sharp interface then:
  fresh feed of 40%/60% graphite pebbles/starting fuel pebbles
  fresh feed of 100% HALEU fuel pebbles
All tests involve OTTO cycle (no recycling)

## Slide 11: Sharp Interface with Starting Fresh Fuel Feed
Fresh feed of 40%/60% graphite pebbles/starting fuel pebbles
Griffin and Kugelpy predict slightly different critical heights (different eigenvalue at t=0)
  Very similar k-eff trend between the two codes
  Differences in predicted critical height a mater for more detailed future investigation
Maximum power density prediction very similar between two codes

## Slide 12: Conclusions and Future Work
Kugelpy and Griffin use completely different methods for running-in calculations
  Similar results seen for key features of running-in simulation including predictions for maximum power density
  Spike in power density had been seen in Griffin simulations previously, but not clear it was a physical result; verification with Kugelpy increases confidence it is a physically correct result
Diffusion with pre-generate multigroup cross section library seemed to work well in this study, but some features from more realistic models still need to be tested like:
  temperature gradients
  void region above core
  control rods
  recycling of pebbles